## Slide 1
AI AND SOLAR POWERED
GRASS CUTTING ROBOT
BEng Robotics & AI · Individual Major Project · Project No. 7-13
Student: Tan Qi Yuan
Student ID: 031DDDDD (PSB) | qt24aae (UH) Supervisor: Wong Kim Siong Date: 09 April 2026
30 wks
project duration
5 / 8
objectives done
ROS2 Kilted
+ SLAM + Nav2
Raspberry Pi 4B
Ubuntu 24.04 LTS

## Slide 2
Introduction & Aims
Why build a solar-powered autonomous grass cutting robot?
⚠ The Problem
Traditional petrol mowers:
• Produce CO₂ and greenhouse gases
• Require manual effort every week
• Cause noise pollution
• Carry operator safety risks
Commercial robot mowers exist but minimum cost $1000+
🎯 Project Aim
To design and develop a low-cost AI solar-powered grass cutting robot for residential lawn maintenance. Integrate AI for navigation and obstacle detection, enabling it to map and plan efficient cutting paths, avoid object in real time, and renewable solar energy to reduce manual effort and promote eco-friendly smart home automation.
✔
Solar charging power system
✔
LIDAR scanning + SLAM mapping + Saved map
✔
2WD teleoperation via ROS2
Cutting mechanism
✗
Camera (object detection + recognition)
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
✗
Localization --> Autonomous Navigation
✗
Real Time Object Avoidance + Plan cutting paths
Printed Chassis & Assembled
✔
✔

## Slide 3
Methodology — System Architecture
Four subsystems connected through Raspberry Pi 4B running ROS2 Kilted
☀️ Power System
2× 4W Dexter Solar Panels (series) [21V / 0.5A]
└─> PWM Solar Charge Controller
└─> 12.6V BMS + 3S3P 18650 Battery [11.1V / 12.6V]
├ LM2596 5V → RPi → LIDAR via USB
├ L298N #1 → 4× DC Drive Motors
└ L298N #2 → 1× DC Cutter Motor
⚙️ Locomotion & Cutting
4× 5V DC Motors — 2WD config
L298N #1 GPIO BCM:
L = 13(IN1) / 19(IN2) / 26(ENA)
R = 5(IN3) / 6(IN4) / 12(ENB)
PWM 1000Hz — teleop via ROS2 (Xterm)
1× 5V DC Motor (Cutter)
L298N #2 GPIO BCM: 16(IN3) / 20(IN4) / 21(ENB)
cutter_controller.py to control the cutter ON/OFF
📡 Sensing
RPLidar A1M8 — USB to RSPi
Scan (/scan) — RVIZ2 ✔
Teleop (/cmd_vel) — ROS2 ✔
SLAM Toolbox — map saved ✔ (.pgm | .yaml)
Camera (Pi Cam) — not working (OS issue)
Ultrasonic + SG90 / LDR — not integrated
💻 Computation & Software
Raspberry Pi 4B (4GB RAM)
Ubuntu Server 24.04 LTS + XFCE (Headless Setup)
Putty SSH + TigerVNC remote access
ROS2 Kilted
Aluminium case + Dual fan cooling
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI

## Slide 4
Results
Summary of what was achieved against each objective
Objective
Status
Notes
Solar charging system
Verified with multimeter. Solar panels insufficient current for whole system operation
2WD Teleoperation
✔ Done
keyboard_teleop → /cmd_vel → GPIO → motors via VNC.
Note: linear speed too fast; turning too slow — PWM tuning needed
LIDAR scanning (RVIZ2) + SLAM mapping + map saved
✔ Done
RPLidar A1M8 → /scan topic verified live in RVIZ2
Occupancy grid maps built and saved via map_saver_cli to ~/robot/maps/ (.pgm | .yaml)
✔ Done
Cutting mechanism
L298N #2 wiring complete (BCM 16/20/21)
Camera integration
✗ No
libcamera incompatible with Ubuntu Server 24.04
Autonomous navigation (Nav2)
✗ No
Nav2 configured and loads saved map. Needs real odometry (no wheel encoders / IMU)
Object Avoidance + Path Planning
RVIZ show object detection. Boustrophedon cutting path plan planned but tested yet
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
✔ Done
✔ Done
3D chassis assembly
Cults3D design printed and assembled at school
✗ No

## Slide 5
Discussion — Key Challenges
What went wrong and how to fix it
💥 SD Card Failure (Biggest Impact)
🌞 Solar Power — Not Enough
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
📷 Camera — OS Incompatibility
Pi Camera needs libcamera stack
libcamera only works on Raspberry Pi OS
Ubuntu Server 24.04 LTS does not support it
🗺️ Nav2 — No Odometry
Nav2 launches + loads saved map ✔
AMCL needs real odometry to localise
No wheel encoders or IMU = position drift
SD card failed Feb 2026 — lost ALL data
~ 2 weeks wasted rebuilding from scratch
No backups were kept (lesson learned)
Pushed autonomous navigation past deadline
2 panels = max 0.5A output
5 motors + LIDAR + RPi need more current under load
Panels only practical for idle battery charging
⚡ Speed Tuning — No Stable
Moves too fast in forward/reverse
Turns too slowly
🏗️ 3D Chassis — Not Customize
Wheel keep touching robot body
No space for more components
No wiring management
Not ready for outdoor use
Temperature high
Sol 1: Git version control
Sol 2: full setup.sh automation script
Sol 3: Buy an extra MicroSD card
Sol 1: Use a standard USB webcam instead
Sol 2: Use a second RPi with RPi OS and let both boards communicate
Sol: Use higher wattage solar panel
Sol 1: Add wheel encoders — Accurate distance + speed per wheel & Add IMU (Inertial Measurement Unit) — Rotation drift, straight-line
Sol 2: Create fake odometry node
Sol 1: Reduce PWM duty cycle in motor_control node
Increase angular gain / angular velocity cap in motor_control node
Sol 1: Design in Fusion 360, make a weatherproof enclosure, implement more cooling fans to reduce high temperature

## Slide 6
Conclusions
✔
Solar charging circuit — BMS + LM2596 stable 5V supply confirmed
✔
2WD teleoperation working — full ROS2 → GPIO → motor pipeline verified
✔
RPLidar A1M8 fully integrated with ROS2 — live scan in RVIZ2 | SLAM mapping complete — maps saved with map_saver_cli (.pgm | .yaml)
✔
Cutting mechanism — safe prototype zip-tie blade
✔
Physical prototype assembled — 3D chassis, all hardware mounted
✗
Object avoidance & path planning not achieved — planned and still working on it
→
Pi Camera, HC-SR04, LDR integration not achieved — Ubuntu Server does not support libcamera libraries & insufficient time
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
✗
✗
Autonomous navigation not achieved — unforeseen SD card failure + no wheel encoders + IMU for odometry

## Slide 7
Further Development
What comes next — in priority order
🗺️ #1 — Immediate
Odometry → Autonomous Navigation
No wheel encoders & IMU
→ Create fake odometry node
→ Nav2 autonomous navigation
→ Boustrophedon cutting path plan
⚡ #2 — Immediate
Motor Speed Tuning
Reduce linear PWM duty cycle
Increase angular speed/gain
☀️ #3 — Short term
Solar Power Upgrade
Use higher wattage solar panel for sustainable charging
💾 #6 — Ongoing
Backup & Version Control
Git version control for all code
Automated weekly SD card
Image backup to network share
🏗️ #7 — Future
Custom Chassis
Design in Fusion 360
Better component fit
Weatherproof enclosure
Cooling system
📱 #8 — Future
Mobile App Control
Use Wi-Fi or Bluetooth to replace keyboard teleop with customize mobile app interface for convenience
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
✂️ #5 — Short term
Cutting Motor
Replace with better motor cutter to cut the grass efficiently
📷 #4 — Short term
Camera → YOLOv8
Switch to USB webcam
→ Camera feed in ROS2
→ YOLOv8 object detection

## Slide 8
Prototype Demo & Q&A
Demo will show:
✔ Raspberry Pi 4B running ROS2 Kilted accessed via VNC
✔ RPLidar A1M8 — live 360° scan in RVIZ2
✔ 2WD teleoperation — motors responding to keyboard commands
✔ Saved SLAM map in ~/robot/maps/ (.pgm | .yaml)
✗ Autonomous navigation — not available (needs more time to create fake odometry)
Project at a Glance
~30 wks
project duration
15 phases
in Gantt chart
5 ✔ done
main objectives
ROS2 Kilted
on Ubuntu Server 24.04
SLAM ✔
map saved
AI & Solar Grass Cutting Robot | Tan Qi Yuan | 9 April 2026 | BEng Robotics & AI
Thank you for listening — Questions Welcome
Thank you for listening — Welcome
GITHUB Link: Stored: Flowchart, Gantt Chart (Old/New), Risk Assessment, Codes
[URL] – https://github.com/Seventy969/IMP
YouTube Link: Stored: Testing & Demo Video
[SolarChargeBatteryTestingURL] – https://youtu.be/AOLYDHLWg1Y
[SolarChargeaControllerTestingURL] – https://youtu.be/r81rF58QbzE
[FullRunDemoURL] – https://youtu.be/DD2j_6H0hDs